Back on tracks

So, during my time at school, I measured the performances of the attenuator and the 2 bandpass filters.It appears that they do not function as they should.
In other words, simulation looks ok, the filter let perfectly through the signal at 1.9 GHz, and attenuates the other frequencies. Measurement showed that the attenuator works as intended.
The 1st filter cuts every frequency. The 2nd one, instead of letting through at 1.9 GHz , it is attenuating even more the signal at 1.9 GHz !

The problem might comes from the choosen inductors. The 1uH inductors used have a SRF of about 60 MHz. It means that beyond this frequency, the inductor won’t behave as a self anymore. It will be a capacitor, or whatever. Everything but an inductor. The next step is either to see if a lower inductor with a 1.9GHz SRF is ok, or if we have to redo the design on Kicad in order to do not have any lumped component that might parasite the signal.

1st , I will put on some lumped elements and see the result. On the 2nd filter, I have some 0603 27 nH inductors with a SRF of 1900 MHz. It might be a solution, or not. I still don’t know for now.
On the 1st filter, the 1uH need to be disoldered and replaced by 1206 inductors with a SRF of 1.9GHz. I don’t have any right now. I will go to ISEN this afternoon and see if there is some. If not, I will order some. For now, I’ll buy some inductors for the coupled microstrip filter at 0603 format. PCB will be then be redisigned.

Also, what I though was biasing resistors were in fact 0 Ohms debugging resistors. After supplying the RF Amp PCB, 2 resistors just died.They burned, along with the pads beneath it.

Concerning the design of amplifier from transistors, instead of doing impedance matching, some « load pull sweep » are done. It seems it is adaptation stuff as well, but in a different way than the impedance matching.