Load pull sweep

It is a method used in advanced HF electronics design in order to maximize the power transfered.
For example,let’s take the TGF3015-SM GaN transistor (specifically used for RF amplification).
The bias used in this case is : 32V and 50 mA. We can see that according to the presented impedances to the transistor (e.g input and output), we get either a maximum power, or gain or best efficiency. You choose what you wish to achieve.
For this, as we designed this summer, we need to make the transistor « see » at the input (for example ! ) an impedance of 25.48 – 42.48*j Ohms and at the output an impedance of 307.16 – 114.94*j. One question remains : do we assume that a « slug » adaptation is good ? (e.g input or output is 50 Ohms when designing the other). Or do we have to make a double stub adaptation (both impedances are not 50 Ohms, which seems to be the case here).
In power transistors for HF, these load pull values for source/load impedances are usually given. No need to use a software in order to calculate it.

Once the prototype is fully working as it is intended to, work on transistors can then seriously begin.