Understanding the concept of AC Power

Who talks about AC power therefore talks about AC signals.

When a signal empowers a purely resistive load (Z = R) , either the voltage and current product is 0 or positive,as they are in phase. Therefore, no power get back towards the source. It is called « Active power » (or real power).It is expressed in Watts.
Ohm’s law : P = I^2/R

When the load is reactive (Z = jX) , it means that voltage and current are 90 degrees out of phase.
In this case, energy is either stored by the reactive components, or delivered to the load.
For a 90 degress out of phase, with two sinusoids, it means that from t = 0 until t=T/4, energy will be stored, as voltage and current are out of phase. From T/4 until T/2 energy will be delivered, as voltage and current are in phase. The reactive power is the one which consumes current, but do nothing. It is not delivered.
We can calculated this reactive power thanks to Ohm’s law : Q = I^2/X, with X the reactance, expressed in Volt-Amps-Reactive (VAR).
We can notice instantaneously that reactive power of an inductor and capacitor can cancelled out. This is the key concept for the conjugate match. Avoid reactive power and maximize the power transmitted.

When dealing with components having both resistive and reactive parts (e.g Z = R + jX), we are talking about apparent power.
P = I^2/Z.

In a good circuit, the true power is as high as we want and will depends on the specification (biaising, wanted output power), reactive power must be as small as possible and therefore apparent power has to be as close as possible from the real power.

What is this famous formula P = (1/2)*Re(V* (I*) ) ?

It is the generic formula in order to know what is the power dissipated in whatever element.
The searched output value is the real power we talked about previsously. V and I are sinusoids. V(t) = Vrms*sin(wt + phiV) and I (t)= Irms*sin(wt + phiI).
The 1/2 term come from the fact that voltage and current amplitudes are expressed by their rms value.
We want the real part, because we want the real power P , not the reactive power Q (Im(V* (I*) ) ) nor the apparent power S (V* (I*) ) . The real power and only this one.

By definition, P = Re(S) = Vrms*Irms*cos(theta), with theta being the phase difference between the voltage and the current (e.g theta = phiV – phiI).
Here we just saw why we take I* and not I. If we do V*I, then we would have Vrms*Irms*cos(phiV+phI), which is different from the expression of P.
Then, we can also talk about the power factor. It is expressed as the ratio between the real power and the apparentpower. The closer to 1 the better.

How conjugate match comes into action ?
Well, let’s imagine a load impedance and a source impedance. Both has resistance and reactance parts in their impedance. We want to minimize the reactance, as it consumes power but do nothing else. We want the reactive parts to cancel each other. That’s all. Conjugate match is not used when designing power amplifier , though, but load pull instead. In fact, when designing the heart of the PA, power match (load pull) is used instead of conugate match. Once this black box is designed, the more classical conugate match is used to design the rest of the circuit.
Conjugate match could be used with power amplifier. However its non linear performance (e.g P1dB for example) would be worse than the load pull match.

How to evaluate if the match is good ?
Thanks to the transducic gain. The latter is expressed as the ration between the power delivered to the load over the power available at the source.
The formula for the power delivered to the load is already know.
As for tor the power available at the source, I found this formula (Jim Stiles, University of Kansas) :

This is the real power very maximum value that the source could deliver to the load, with Rg the source resistance and Vg the source sinusoid voltage.