Overview about power amplifiers

If we wish to calculate the RF power in the frequency domain : P = 1/2(V*(i*).
And in the time domain :	1/2(Vpp*Ipp)*cos(phi), with pp being the peak to peak value.

However, if we want the total power in the frequency domain : (V*(i*))
And in the time domain : 1/8(Vpp*Ipp)*cos(phi)

Phi represents the phase delay between the two waves.

These 2 stands for the average power dissipated by the device.

As the time domain average power is a cosine defined fucntion, power will vary from (Vpp*Ipp)/8
to -((Vpp*Ipp)/8.
If Pavg is positive, it means that current and voltage are in phase, so power is dissipated as heat.
If Pavg is negative, it means that current and voltage are out of phase, meaning that power is being generated.
If Pavg is nil, power is not generated nor dissipated. It is being stored instead.