## Slide 1: 2018 Semester#1 Analog Circuits Design AFL axel.flament@YNCREA.fr

## Slide 2
Physical structure and modes of operation
Operation of the NPN in Active Mode
PNP Transistor, circuit symbols
Graphical representation of Transistor characteristics
Analysis of transistor circuits at DC
The BJT as an amplifier
Small-signal equivalent model
Bipolar Junction Transistor

## Slide 3: BJT - Intro
3 terminal device : Base, Emitter, Collector
Principle : Use of a voltage between 2 terminals to control the current flowing in the 3rd terminal  « controlled source »
+ : High-frequency operation, reliability, high-current driving capabilities
- : « not-so-high » input impedance, power consuming
Bipolar : holes and electrons are involved in current

## Slide 4: Physical structure and modes of operation
For amplifier design, we only use Active mode !

## Slide 5
Physical structure and modes of operation
Operation of the NPN in Active Mode
PNP Transistor, circuit symbols
Graphical representation of Transistor characteristics
Analysis of transistor circuits at DC
The BJT as an amplifier
Small-signal equivalent model
Bipolar Junction Transistor

## Slide 6: Operation of the NPN in Active Mode
Assume the active mode : EBJ is forward-biased, CBJ is reversed-biased :
  VBE ~ 0,6V
  VBC<< 0,6V
IC = IS exp(VBE / Vt)
  IC is the collector current
  IS is the saturation current (depending on geometry of the base, doping, etc…)
  VBE is the base-emitter voltage
  Vt is the thermal voltage = kT/q = 25mV @ 25°C, with k = Boltzmann constant, T the room temperature and q the electron charge
IC = β IB, β is the common-emitter current gain (depending on geometry, doping…), from 50 to 1000 ! Usually : 100-200
IE = IC + IB (or IC = αIE )
NPN
B
C
E
IB
IE
IC
Vbe
Vbc

## Slide 7: Operation of the NPN in Active Mode-exercices
Consider a NPN transistor with VBE = 0,7V @ IC = 1mA. Find VBE for IC=0,1mA and IC=10mA.
Transistors of a certain type are specified to have β values in the range of 50 to 150. Find their α values
Measurement of an NPN BJT in a particular circuit shows the base current to be 14,46µA, the emitter current to be 1,46mA and VBE = 0,7V. Calculate α, β and IS
Calculate β of 2 transistors for which α = 0,98 and 0,99. For collector currents of 10mA, find the base current of each transistor

## Slide 8: Operation of the NPN in Active Mode
Cross section of an NPN BJT
Not symmetrical, emitter and collector can not be interchanged !

## Slide 9
Physical structure and modes of operation
Operation of the NPN in Active Mode
PNP Transistor, circuit symbols
Graphical representation of Transistor characteristics
Analysis of transistor circuits at DC
The BJT as an amplifier
Small-signal equivalent model
Bipolar Junction Transistor

## Slide 10: NPN & PNP Transistors – representation and conventions
VBE NPN = 0,7V
VBE PNP = -0,7V
Currents are positive

## Slide 11: Summary of BJT I-V relationships in active mode

## Slide 12: Ex
This transistor has β=100 and VBE = 0,7V@IC=1mA
Design the circuit (i.e. find the values of resistances) so that a current of 2mA flows through the collector and a voltage of +5V appears at the collector. Verify that the transistor is in the active mode.
Repeat the exercise with power supplies of ±1,5V, VBE = 0,8V@IC=1mA. (IC = 2mA and VC = 0,5V)

## Slide 13: EX
In this circuit, measurement indicates VB to be 1V and VE to be 1,7V. What are β and α for this transistor? What is the voltage VC?

## Slide 14
Physical structure and modes of operation
Operation of the NPN in Active Mode
PNP Transistor, circuit symbols
Graphical representation of Transistor characteristics
Analysis of transistor circuits at DC
The BJT as an amplifier
Small-signal equivalent model
Bipolar Junction Transistor

## Slide 15: Graphical representation of Transistor characteristics
IC = IS exp(VBE/Vt)
Identical to the diode i-v relationship
At constant current, VBE changes by -2mV/°C

## Slide 16: Dependence of Ic on Vc – Early Effect
VA is the Early voltage (typ. 50 to 100V)
IC = [IS exp(VBE/Vt)](1+VCE/VA)
r0 = (δIC/ δVCE)-1@VBE=cst
Solving it into the IC equation,
we find that
r0=(VA+VCE)/IC = VA/IC’ (current without Early Effect)
(r0 is the output resistance looking
into the collector)

## Slide 17: Graphical representation of Transistor characteristics Exercises
Find the output resistance of a BJT for which VA=100V at IC = 0,1mA, 1mA, 10mA
Consider a BJT for which VA=100V. At VCE=1V, VBE is adjusted to yield a collector current of 1mA. VCE is then raised to 11V (and the same VBE is maintained). What is the new value of IC?
For this circuit, find the voltage VBB that results in the transistor to operate (a) in the active mode with VC=5V, (b) at the edge of saturation (VCE=0,3V), (c) in deep saturation (VCE=0,2V, βforced =10). For simplicity, assume that VBE = 0,7V=cst and β=50

## Slide 18
Physical structure and modes of operation
Operation of the NPN in Active Mode
PNP Transistor, circuit symbols
Graphical representation of Transistor characteristics
Analysis of transistor circuits at DC
The BJT as an amplifier
Small-signal equivalent model
Bipolar Junction Transistor

## Slide 19: Analysis of transistor circuits at DC
In which mode is the transistor operating?
Suppose it is the active mode…calculate each currents and voltages…and verify !
β = 100
Assume VBE =cst= 0,7V
Re-do the exercise with VB=6V
Re-re-do the exercise with VB=0V

## Slide 20: Analysis of transistor circuits at DC
Determine the voltage at all nodes and the current through all branches
Is the mode of operation sensitive to β ?
Find the largest value of RC ensuring the transistor to be in the active mode
Redesign the circuit to have IC=1mA and VCB=-4V

## Slide 21: Analysis of transistor circuits at DC
Find all the voltage and currents (β=100)
Is the mode of operation sensitive to β ?
Find all the voltage and currents (β=100)
Find all the voltage and currents (β=100)

## Slide 22: Analysis of transistor circuits at DC
Find all the voltages and currents (β=100)
What is the total current drawn from the supply? Hence find the power dissipated in the circuit

## Slide 23
Physical structure and modes of operation
Operation of the NPN in Active Mode
PNP Transistor, circuit symbols
Graphical representation of Transistor characteristics
Analysis of transistor circuits at DC
The BJT as an amplifier
Small-signal equivalent model
Bipolar Junction Transistor

## Slide 24: The BJT as an amplifier
When operating in active mode, the BJT behaves as a voltage-controlled current source
  VBE controls IC
  But non-linear relationship… (discussed later)
We have seen that VCCS is the base of transconductance amp, but we are interested in voltage amp
How to transform a current to a
voltage?
Vo =VCC – RCIC
Vo =VCC – RCIS exp(VBE/VT)
Non linear !!

## Slide 25: The BJT as an Amplifier
Biased somewhere in the sloppy region
Input signal is VBEbias + VBE signal
VBEsignal must be small !
This is how linear amplification is achieved with a strongly non linear device

## Slide 26: Small-signal voltage gain
If VBEsignal is small, the output voltage will be nearly proportional to VBEsignal with a gain that is the slope of the characteristic
=( ) @ VBEbias
Or VCE =VCC – RCIS exp(VBE/VT)
AV = – RCIS exp(VBE/VT) / VT = – RC (IC / VT )

## Slide 27: Small-signal voltage gain ex
Consider a amp circuit using a BJT (IS=10-15A, RC = 6,8kΩ, VCC=10V)
Determine the value of VBE required to operate at VCE=3,2V. What is the value of IC ?
Find the voltage gain at that point.
Find the positive increment of VBE that will lead to saturation (VCEsat = 0,3V)
Find the negative increment of VBE that will lead to within 1% cut-off (VCE = 0,99VCC)
Find the value of RC that will give a gain of -320
What is the largest negative swing at the output? What is the corresponding input signal largest swing (suppose amp is linear)?

## Slide 28: Load-line and biasing
Trade-off : gain vs swing

## Slide 29
Physical structure and modes of operation
Operation of the NPN in Active Mode
PNP Transistor, circuit symbols
Graphical representation of Transistor characteristics
Analysis of transistor circuits at DC
The BJT as an amplifier
Small-signal equivalent model
Bipolar Junction Transistor

## Slide 30: Small-signal operations and models
IC = IS exp(VBE/VT)
VBE = VBEbias + VBEsignal
IC = IS exp((VBEbias + VBEsignal )/VT)
= IS exp(VBEbias/VT) exp(VBEsignal/VT)
If VBEsignal is small (<<VT) :
exp(VBEsignal/VT) ~ 1+ VBEsignal/VT
So IC = IS exp(VBEbias/VT) (1+VBEsignal/VT) = ICbias (1+VBEsignal/VT)
ICsignal = ICbias . VBEsignal/VT = gm VBEsignal with gm = ICbias/VT
IBsignal = ICsignal / β = gm VBEsignal / β
The impedance seen from the base is VBEsignal / Ibsignal = β/gm = rπ

## Slide 31: Small-signal operations and models
Hybrid П-model (valid for both NPN and PNP with no change in polarities!)

## Slide 32: Small-signal operations and models
Methodology
  Eliminate signal sources
  Calculate DC voltages and currents
  Calculate the small-signal parameters (gm and rπ )
  Replace the BJT with its small-signal model
  Eliminate DC sources
  Analyze the circuit (input/output impedance, gain)

## Slide 33: Small-signal operations and models
Determine the voltage gain (β=100) for both circuits
Assume that vi has a triangular waveform, determine the maximum amplitude that vi is allowed to have. Then, with the amplitude of vi set to this value, give the waveforms of the total quantities iB(t), vBE(t), iC(t), and vC(t).

## Slide 34: Small-signal operations and models
Augmenting the model with Early Effect
  r0 = VA/ICbias

## Slide 35
gm = ICbias/VT
rπ = β/gm
r0 = VA/ICbias

## Slide 36: Small-signal exercise

## Slide 37: Summary