## Slide 1: 2018 Semester#1 Analog Circuits Design AFL axel.flament@YNCREA.fr

## Slide 2
Characterizing amplifiers
3 basic configurations
The common-emitter amp
The common-emitter amp with an emitter resistance
The common-base amp
The common-collector amp or emitter follower
Biasing in BJT amps
Common-emitter Full Design
Summary
Basic BJT Amplifiers configurations

## Slide 3: Characterizing amplifiers
Rin
  Voltage dividing effect
  May depend on RL
Av0, open-circuit voltage gain
  Vo/Vi when RL is infinite
Rout
  Calculated when Vsig = 0
  Does not depend on Rsig
  Voltage dividing effect

## Slide 4
Characterizing amplifiers
3 basic configurations
The common-emitter amp
The common-emitter amp with an emitter resistance
The common-base amp
The common-collector amp or emitter follower
Biasing in BJT amps
Common-emitter Full Design
Summary
Basic BJT Amplifiers configurations

## Slide 5: 3 basic configurations
Connect 1 of the 3 terminals to ground, thus creating a 2-port networks with the grounded terminal being common to the input and output ports

## Slide 6
Characterizing amplifiers
3 basic configurations
The common-emitter amp
The common-emitter amp with an emitter resistance
The common-base amp
The common-collector amp or emitter follower
Biasing in BJT amps
Common-emitter Full Design
Summary
Basic BJT Amplifiers configurations

## Slide 7: Common-Emitter amp
Most used amp
RC is part of the amp
  A load will appear in parallel with RC
Rin ? Av0 ? Rout?

## Slide 8: Analysis
Replace BJT by its small-signal equivalent model
V0 = -gmvπ(r0//RC)  V0/Vi = -gm(r0//RC)

## Slide 9: Observations
Rin = rπ = β/gm, moderate to low value (range of kΩ). Directly depending on β and inversely proportional to IC. To obtain a higher input res, IC must be lowered but this lowers the gain (trade-off).
RO is moderate to high in value (range of kΩ). To lower RO, RC should be reduced, but it reduces the gain as well
Gain is high, but the bandwidth is limited (we will see it later)

## Slide 10: Common-emitter ex
A common-emitter amp utilizes a BJT with β=100, and VA=100V, is biased at IC = 1mA and has a collector resistance RC = 5kΩ. Find Rin, R0, and AV0. If the amp is fed with a signal source having a res RS = 5kΩ, and a load res RL = 5kΩ is connected to the output terminal, find the resulting gain.

## Slide 11
Characterizing amplifiers
3 basic configurations
The common-emitter amp
The common-emitter amp with an emitter resistance
The common-base amp
The common-collector amp or emitter follower
Biasing in BJT amps
Common-emitter Full Design
Summary
Basic BJT Amplifiers configurations

## Slide 12: The common-emitter amp with an emitter resistance
Connecting a res at the emitter leads to several major changes in common-emitter amp characteristics…
Rin ? RO? AV0? (neglect the Early effect)

## Slide 13: The common-emitter amp with an emitter resistance
Rin= rπ + (β+1)RE
R0 = RC
Av0 ~ -gmRC/(1+gmRE) ~ -RC/RE
Comparison with the CE amp :
Rin is much higher
The gain is much lower (by the same amount) – trade-off !
Input dynamic is improved
The overall gain is less dependent on β
BW is significantly improved (we will see it later)
RE provides negative feedback that stabilizes IC (out of scope)
RE is called Emitter degeneration resistance
This amp is called a degenerated common-emitter

## Slide 14
Characterizing amplifiers
3 basic configurations
The common-emitter amp
The common-emitter amp with an emitter resistance
The common-base amp
The common-collector amp or emitter follower
Biasing in BJT amps
Common-emitter Full Design
Summary
Basic BJT Amplifiers configurations

## Slide 15: The common-base amp
Rin ? RO? AV0? (neglect the Early effect)

## Slide 16: The common-base amp
Rin= rπ / (β+1)
R0 = RC
Av0 ~ gmRC
Observations :
Rin is very low (not so good, except for specific applications)
The gain is high
Rout is high
BW is very good (we will see it later)

## Slide 17: Common-Base Amp EX
Consider a CB amp utilizing a BJT (β=100) biased at IC = 1mA and with RC = 5kΩ. Determine Rin, AV0 and R0. If the amp is loaded with RL = 5kΩ what value of AV results? What is the overall gain if Rsig = 5kΩ?
A CB amp is required to amplify a signal delivered by a coaxial cable having a characteristic res of 50 Ω. What bias current IC should be utilized to obtain Rin that is matched to the cable res? To obtain an overall voltage gain of 40V/V, what should the total res in the collector (i.e. RC//RL) be?

## Slide 18
Characterizing amplifiers
3 basic configurations
The common-emitter amp
The common-emitter amp with an emitter resistance
The common-base amp
The common-collector amp or emitter follower
Biasing in BJT amps
Common-emitter Full Design
Summary
Basic BJT Amplifiers configurations

## Slide 19: The common-collector amp or emitter follower
Rin ? RO? AV0?

## Slide 20: The common-collector amp or emitter follower
Rin= rπ + (β+1)RL
R0 = (rπ + Rsig) / (β+1)
Av0 ~ gmRE / (1+ gmRE) ~ 1
Observations :
Rin is high
The voltage gain is close to unity (but current gain is very high)
Rout is low
Bilateral… (out of scope)
Acts as a buffer amp !

## Slide 21
Characterizing amplifiers
3 basic configurations
The common-emitter amp
The common-emitter amp with an emitter resistance
The common-base amp
The common-collector amp or emitter follower
Biasing in BJT amps
Common-emitter Full Design
Summary
Basic BJT Amplifiers configurations

## Slide 22: BIASING in BJT amps
Biasing = establish a constant DC current in the collector of the BJT
  Predictable current
  Insensitive to variations (temp, β)
  Allow maximum output swing

## Slide 23: BIASING in BJT amps
Bad

## Slide 24: BIASING in BJT amps ex
Figure 1a:
What is the value of VB? (neglect IB)
Find IC (IS = 85fA, T = 300K, no Early effect, VT = 25,8mV)
If R2 is 5% higher and R1 5% lower than their nominal values, what does IC value become?
Figure 1b:
What is the value of IC? (neglect IB, VBE = 0,6V)
Write the relationship between VB, VBE and IC (VB= VE+VBE…)
By differentiating the latter equation, find a condition that make IC variations (as a function of VB) independent of BJT parameters. If we have the same VB variations as in the 1st figure, what would IC be?

## Slide 25: BIASING in BJT amps
Classical discrete-circuit bias arrangement
High R1 and R2 ensure low power consumption
Low R1 and R2 ensure insensitivity to β…
A 2-power-supply version :

## Slide 26: BIASING in BJT amps
Collector-to-Base Feedback res :
RB provides negative feedback
Care must be taken not to forward-
bias Collector-base diode
Using a constant current source
Independent of β and RB !
We will see later how to design
a current source

## Slide 27
Characterizing amplifiers
3 basic configurations
The common-emitter amp
The common-emitter amp with an emitter resistance
The common-base amp
The common-collector amp or emitter follower
Biasing in BJT amps
Common-emitter Full Design
Summary
Basic BJT Amplifiers configurations

## Slide 28: BJT amp – common emitter example – full design
Bypass or decoupling Cap (low impedance to ground for signal)
Coupling Cap (low impedance for signal, high impedance for DC in order not to disturb biasing)

## Slide 29: Other configurations ex

## Slide 30
Characterizing amplifiers
3 basic configurations
The common-emitter amp
The common-emitter amp with an emitter resistance
The common-base amp
The common-collector amp or emitter follower
Biasing in BJT amps
Common-emitter Full Design
Summary
Basic BJT Amplifiers configurations

## Slide 31: Standards voltage Gains formulas

## Slide 32: Standard impedances expressions