## Slide 1: 2018 Semester#1 Analog Circuits Design AFL axel.flament@YNCREA.fr

## Slide 2
Current sources – introduction
Current mirrors
Active loads
Current mirrors and active loads

## Slide 3: Introduction
We have seen the full design schematic
  Almost full design : current source is missing

## Slide 4: Introduction
In IC chips with a lot of amplifiers, a constant DC current is generated at one location and then replicated next to the amps (current steering)
Because the effort of a stable, precise, current source is only made once, and not for every amp !
How to duplicate current from a nice and clean current reference?
The idea is that BJTs are voltage-controlled current sources
If 2 BJTs share the same VBE, they will “produce” the same current

## Slide 5: Introduction – the basic BJT current mirror
Ideally :
  I0 = Iref or a multiple part of it
  The output impedance of the current source is infinite

## Slide 6
Current sources – introduction
Current mirrors
Active loads
Current mirrors and active loads

## Slide 7: Basic current mirror
Q1 and Q2 must operate in the active mode !
  VCEQ2 > 0,3V
I0/Iref = IS2/IS1 = Emitter Area of Q2/emitter area of Q1
Use of transistors in parallel if the ratio is an integer
β is finite…
  Iref = IC +2 IC/β
  So I0/Iref = 1/(1+2/β)
  β=100  error = 2%
Output res is R0 = VA/I0
  I0 = Iref only when VCEs are equal
  I0 = Iref ( 1+ (V0-VBE)/VA)

## Slide 8: Basic current mirror - ex
Consider a BJT current mirror with a nominal current transfer ratio of 1. The BJTs have IS = 1e-15A, β=100, VA=100V. For Iref=1mA, find I0 when V0=5V. Find the output resistance.

## Slide 9: Improved current mirrors
Base-current compensation
  I0/Iref = 1/(1+2/(β²+ β))
    β=100  error = 0,02%
  R0 = VA/I0

## Slide 10: Improved current mirrors
Wilson current mirrors
  I0/Iref = 1/(1+2/(β(β+2))
  R0 = β3 x R03 /2
  But : additional VBE drop
  for good operation

## Slide 11: Improved current mirrors
Widlar current mirrors
  VBE1 = VT ln(Iref/IS)
  VBE2 = VT ln(I0/IS)
  VBE2 – VBE1 = VT ln(I0/Iref)
  I0RE = VT ln(I0/Iref)
Error is similar to the basic current
source
Rout ~ r0 ( 1+ gm (RE//rπ))
Pros : generate low current with
« not so high » resistors / High output res

## Slide 12: Current ratio
R2I2 = R1I1 + VTln(I2 IS1 /Iref IS2)
error
I2 = I1 (R1/R2)+ VTln(I2/Iref) / R2
The error can be canceled if the BJT
emitter area is equal to the ratio of
desired currents (ratio of resistances)

## Slide 13: Current Mirrors Ex

## Slide 14: Current Mirrors Ex

## Slide 15: Current Mirrors Ex

## Slide 16: Current Mirrors Ex

## Slide 17: Current Mirrors Ex

## Slide 18
Current sources – introduction
Current mirrors
Active loads
Current mirrors and active loads

## Slide 19: Active loads
Basic gain cell : CE
RC is replaced by a current-source
  Difficult to implement high and precise
  value of res in IC
  Output res of current-source is very high
  Good for high gain !
The CE is said to be “current-source loaded” or “active loaded”

## Slide 20: Active Loads
Gain = gm1 x (r01//r02)
r01= r02 because VA1=VA2 and IC1=IC2
Gain = (IC1/VT) x r01/2
Gain = (IC1/VT) x VA/2IC1
Gain = VA/2VT = 20 VA

## Slide 21: Increasing voltage gain again
How can we increase the gain??
  Circuit that passes the
  gm1Ve current from Q1 to Q2 but exhibits
  a much larger output impedance
  Current buffer (pass the current
  and raise the resistance level)
  Common-base circuit can achieve this !
    Current gain is 1
    Output impedance is high
  This circuit is called a cascode
  One can also cascode the current source…

## Slide 22: Active loads ex