## Slide 1: 2018 Semester#1 Analog Circuits Design AFL axel.flament@YNCREA.fr

## Slide 2
Introduction
Emitter Follower
Class of operation
Thermal considerations
Output stages and Power Amplifiers

## Slide 3: Output stages and PA - introduction
Delivers signal to the load
  Small output impedance
Small-signal approximation must be used with care
Linearity is important
  THD (Total Harmonic Distortion) ~ 0,1% for Hi-Fi audio PA
Efficient
  Dissipated power in the output transistors must be low (junction temperature proportional to Pdiss)
  η = Pdelivered to the load / Pdelivered from the supplies

## Slide 4
Introduction
Emitter Follower
Class of operation
Thermal considerations
Output stages and Power Amplifiers

## Slide 5: Emitter follower
iE = I + IL
I must be greater than the largest negative IL to ensure Q1 always operates in active-mode
Class A
VO = VI – VBE1
V0max = VCC – VCEsatQ1
V0min = -IRL (Q1 is off)
Or Vomin = –VCC + VCEsatQ2 (Q2 saturates)
  if I>|- VCC + VCEsatQ2 | / RL)

## Slide 6: Emitter follower - ex
For this amp, VCC=15V, VCEsat = 0,2V, VBE = 0,7V, β is very high. Find R to establish a bias current sufficiently large to allow the largest possible output swing for RL = 1kΩ (Q3 is a current mirror). Determine the resulting output signal swing and the min and max emitter currents for Q1
For this amp, I = 14,8mA, consider the case in which V0 is limited to the range -10V to +10V (VBEQ1=0,6V @ IEQ1 = 1mA, α = 1). Find VI corresponding to V0 = -10, 0 and +10V. At each of these points, use small-signal analysis to determine the gain VO/VI.

## Slide 7: Emitter follower - Waveforms
RL = VCC/I

## Slide 8: Emitter Follower - Ex
For this amp, VCC=10V, I=100mA, and RL=100Ω.
Find the power dissipated in Q1 and Q2 under quiescent conditions (V0=0V)
For a sinusoidal output voltage of maximum possible amplitude (neglecting VCEsat), find the average power dissipation in Q1 and Q2. Find the load power. (Hint : sketch the waveforms)

## Slide 9: Emitter follower - Efficiency
  η = Pdelivered to the load / Pdelivered from the supplies (average values !)
PL = V0rms²/RL = 0,5 V0pk²/RL = 0,5 VCC²/RL = 0,5 VCC I
Pdelivered = PVCC + P-VCC = VCC IEQ1 + (-VCC) IEQ2
= VCC I + (-VCC) (-I)
= 2 VCC I
η = V0pk²/(4VCCRLI)
= 25% (best case)
RL = VCC/I

## Slide 10: Emitter follower - EX
VCC=10V, I=100mA, RL = 100Ω
If the output voltage is a 8Vpk sinusoid, find :
  The power delivered to the load
  The average power drawn from the supplies
  The power-conversion efficiency

## Slide 11
Introduction
Emitter Follower
Classes of operation – efficiency improvement
Thermal considerations
Output stages and Power Amplifiers

## Slide 12: Issue
How to improve PA efficiency?
  Pdelivered to the load will always be V0rms²/RL
  Pdelivered from the supplies can be lowered if output transistors do not conduct all the time…
We can imagine that Q1 and/or Q2 can conduct for a certain amount of time, reducing power consumption
PAs are classified relatively to their transistor conduction time
This one is a class A PA (Q1 always conducting)

## Slide 13: Class of operation
IQ decreases  consumption decreases, efficiency increases !

## Slide 14: Class B PA
vI = 0 : both BJTs are off, V0=0
When vI rises and exceeds about 0,5V, QN starts conducting and acts as a Emitter Follower : V0 = VI-VBEN, QP is off
When vI goes negative, same behavior with QP
Class B PA is biased at zero current and conducts only when signal is present
Other name : Push-pull (QN pushed the current into the load, QP pulls the current from the load)
(strictly speaking, it is a class C, because of non-zero VBEs)

## Slide 15: Class B PA
V0max = VCC-VCEsatN
  vI max = VCC-VCEsatN + VBEN
Vomin= -VCC-VCEsatP
  vI min = -VCC-VCEsatP + VBEP
Cross-over distortion !

## Slide 16: Class B efficiency
  η = Pdelivered to the load / Pdelivered from the supplies (average values !)
PL = V0rms²/RL = 0,5 V0pk²/RL = 0,5 VCC²/RL
Pdelivered = PQN + PQP = VCC IEQN + (-VCC) (-IEQP)
= VCC V0pk/(pi RL) - VCC (-V0pk/(pi RL))
= VCC²/(pi RL) + VCC²/(pi RL)
= 2VCC²/(pi RL)
η = pi/4 = 78,5% (best case)

## Slide 17: Class B – Power dissipated by transistors
Pdiss = Psupplies – Pload
= 2VCC V0pk/(pi RL) - 0,5 V0pk²/RL
The worst case is found by differentiating this equation :
  V0pk = 2VCC/pi
Pdiss max = 2VCC²/ (pi²RL)

## Slide 18: Class B - ex
It is required to design a class B output stage to deliver an average output power of 20W to an 8Ω load. The power supply is to be selected such that VCC is about 5V greater than the pk voltage (This avoids transistor saturation and the associated nonlinear distortion). Determine the supply voltage required, the pk current drawn from each supply, the total supply power, and the power-conversion efficiency. Determine the maximum power that each transistor must be able to dissipate safely.

## Slide 19: Class B - ex
For this class B PA, let VCC=6V and RL = 4Ω. If the output is a sinusoid with 4.5Vpk amplitude, find:
  The output power
  The average power drawn from each supply
  The power efficiency obtained at this output voltage
  The peak currents supplied by vI, assuming βN = βP =50
  The max power that each transistor must be capable of dissipating safely

## Slide 20: Class AB
In order to get rid of cross-over distortion, QN and QP could be biased at a small non-zero current (class AB)
When vI rises, VBN rises by the same amount V0= VI+VBB/2-VBEN, iN rises, so VBEN rises, so VBEP decreases
For power calculation, it is the same as class B except that each transistor dissipates VCCIQ @ VI = 0

## Slide 21: Generating VBB
Diodes biasing
Thermal feedback
IR = VBE1/R1
VBB = (R1+R2)IR = VBE1 (1+R2/R1)
VBE multiplier
Thermal feedback

## Slide 22: VBE multiplier - ex
Consider a VBE multiplier with R1=R2=1.2kΩ, utilizing a transistor that has VBE=0,6V @ IC=1mA, and a very high β. Find the value of the current Ibias that should be supplied to the multiplier to obtain a terminal voltage of 1,2V. Find the value of Ibias that will result in the terminal voltage changing from the 1,2V value by +50mV, +100mV, +200mV, -50mV, -100mV, -200mV

## Slide 23
Introduction
Emitter Follower
Class of operation
Thermal considerations
Output stages and Power Amplifiers

## Slide 24: Thermal considerations – power BJT
Transistors that must conduct currents in the Ampere range and to withstand power in the W – tens of W range differ in their physical structure, packaging, specifications from the small-signal transistors considered before…
The dissipated power is converted into heat, which raises the junction temperature TJ. Above TJmax (150-200°C) the transistor may be destroyed !
The heat will be conducted from the junction to the case, and from the case to the ambient air : TJ-TA = θJA Pdiss where θJA is the thermal resistance between junction and ambient air
θJA must be low (depends mainly on packaging, specified in datasheets)

## Slide 25: Thermal considerations – Ex
Power-derating curve
A BJT is specified to have a max Pdiss of 2W at an ambient temperature TA0 of 25°C and a TJmax of 150°C. Find the thermal resistance, the maximum power that can be dissipated @ TA = 50°C, and TJ if the device is operating at TA = 25°C and is dissipating 1W.

## Slide 26: Thermal resistance
θJA = θJC + θCA
θJC is fixed by the device and packaging
Can be reduced when a large metal plate is in contact with the collector (ex: TO3)
The circuit designer can reduce θCA, by means of bolting the transistor into a larger metal surface (heat sink)
θCA = θCS + θSA, can be low !

## Slide 27: Thermal resistance - EX
A BJT is specified to have TJmax = 150°C and to be capable of dissipating maximum power as follows :
  40W@TC=25°C,
  2W @ TA = 25°C.
Above 25°C, the maximum power dissipation is to be derated linearly with θJC = 3,12°C/W and θJA = 62,5°C/W
Find the maximum power that can be dissipated safely by this transistor when operated in free air (TA=50°C)
Find the max power that can be dissipated safely when operated at TA=50°C, but with a heat sink for which θCS = 0,5°C/W and θSA = 4°C/W. Find TC and TS
Find the max power that can be dissipated safely if an “infinite heat sink” is used at TA=50°C