### - Qucs - Quite Universal Circuit Simulator
# Short Description of Mathematical Functions

The following operations and functions can be applied in Qucs equations. For detailed description please refer to the "Measurement Expressions Reference Manual". Parameters in brackets "[]" are optional.
## Operators
### Arithmetic Operators
+x	Unary plus
-x	Unary minus
x+y	Addition
x-y	Subtraction
x*y	Multiplication
x/y	Division
x%y	Modulo (remainder of division)
x^y	Power

### Logical Operators
!x	Negation
x&&y	And
x||y	Or
x^^y	Exclusive or
x?y:z	Abbreviation for conditional expression "if x then y else z"
x==y	Equal
x!=y	Not equal
x<y	Less than
x<=y	Less than or equal
x>y	Larger than
x>=y	Larger than or equal

## Alphabetical List of Functions
abs adjoint angle arccos arccosec arccot arcosech arcosh arcoth arcsec arcsin arctan arg arsech arsinh artanh avg besseli0 besselj bessely ceil conj cos cosec cosech cosh cot coth cumavg cumprod cumsum dB dbm dbm2w ddx deg2rad det dft diff erf erfc erfcinv erfinv exp eye fft fftshift fix floor Freq2Time GaCircle GpCircle hypot idft ifft imag integrate interpolate inverse kbd length limexp linspace ln log10 log2 logspace mag max min Mu Mu2 NoiseCircle norm phase PlotVs polar prod rad2deg random real rms Rollet round rtoswr rtoy rtoz runavg sec sech sign sin sinc sinh sqr sqrt srandom StabCircleL StabCircleS StabFactor StabMeasure stddev step stos stoy stoz sum tan tanh Time2Freq transpose twoport unwrap variance vt w2dbm xvalue ytor ytos ytoz yvalue ztor ztos ztoy
## Math Functions
### Vectors and Matrices: Creation
eye(n)	Creates n x n identity matrix
length(y)	Returns the length of the given vector
linspace(from,to,n)	Creates a real vector with n linearly spaced components between from and to, both inclusively
logspace(from,to,n)	Creates a real vector with n logarithmically spaced components between from and to, both inclusively

### Vectors and Matrices: Basic Matrix Functions
adjoint(x)	Adjoint matrix of x (transposed and conjugate complex)
det(x)	Determinant of a matrix x
inverse(x)	Inverse matrix of x
transpose(x)	Transposed matrix of x (rows and columns exchanged)

### Elementary Mathematical Functions: Basic Real and Complex Functions
abs(x)	Absolute value, magnitude of complex number
angle(x)	Phase angle in radians of a complex number. Synonym for arg()
arg(x)	Phase angle in radians of a complex number
conj(x)	Conjugate of a complex number
deg2rad(x)	Converts phase from degrees into radians
hypot(x,y)	Euclidean distance function
imag(x)	Imaginary part of a complex number
mag(x)	Magnitude of a complex number
norm(x)	Square of the absolute value of a vector
phase(x)	Phase angle in degrees of a complex number
polar(m,p)	Transform from polar coordinates (magnitude m, phase p) into complex number
rad2deg(x)	Converts phase from radians into degrees
real(x)	Real part of a complex number
sign(x)	Signum function
sqr(x)	Square (power of two) of a number
sqrt(x)	Square root
unwrap(p[,tol[,step]])	Unwraps the angle p (in radians -- default step is 2*pi) using the optional tolerance value tol (default is pi)

### Elementary Mathematical Functions: Exponential and Logarithmic Functions
exp(x)	Exponential function to basis e
limexp(x)	Limited exponential function
log10(x)	Decimal logarithm
log2(x)	Binary logarithm
ln(x)	Natural logarithm (base e )

### Elementary Mathematical Functions: Trigonometry
cos(x)	Cosine function
cosec(x)	Cosecant
cot(x)	Cotangent function
sec(x)	Secant
sin(x)	Sine function
tan(x)	Tangent function

### Elementary Mathematical Functions: Inverse Trigonometric Functions
arccos(x)	Arc cosine (also known as "inverse cosine")
arccosec(x)	Arc cosecant
arccot(x)	Arc cotangent
arcsec(x)	Arc secant
arcsin(x)	Arc sine (also known as "inverse sine")
arctan(x[,y])	Arc tangent (also known as "inverse tangent")

### Elementary Mathematical Functions: Hyperbolic Functions
cosh(x)	Hyperbolic cosine
cosech(x)	Hyperbolic cosecant
coth(x)	Hyperbolic cotangent
sech(x)	Hyperbolic secant
sinh(x)	Hyperbolic sine
tanh(x)	Hyperbolic tangent

### Elementary Mathematical Functions: Inverse Hyperbolic Functions
arcosh(x)	Hyperbolic area cosine
arcosech(x)	Hyperbolic area cosecant
arcoth(x)	Hyperbolic area cotangent
arsech(x)	Hyperbolic area secant
arsinh(x)	Hyperbolic area sine
artanh(x)	Hyperbolic area tangent

### Elementary Mathematical Functions: Rounding
ceil(x)	Round to the next higher integer
fix(x)	Truncate decimal places from real number
floor(x)	Round to the next lower integer
round(x)	Round to nearest integer

### Elementary Mathematical Functions: Special Mathematical Functions
besseli0(x)	Modified Bessel function of order zero
besselj(n,x)	Bessel function of first kind and n-th order
bessely(n,x)	Bessel function of second kind and n-th order
erf(x)	Error function
erfc(x)	Complementary error function
erfinv(x)	Inverse error function
erfcinv(x)	Inverse complementary error function
sinc(x)	Sinc function (sin(x)/x or 1 at x = 0)
step(x)	Step function

### Data Analysis: Basic Statistics
avg(x[,range])	Arithmetic average of vector elements; if a range is given then x must have a single data dependency
cumavg(x)	Cumulative average of vector elements
max(x,y)	Returns the greater of the values x and y
max(x[,range])	Maximum value in vector; if a range is given then x must have a single data dependency
min(x,y)	Returns the lesser of the values x and y
min(x[,range])	Minimum value in vector; if a range is given then x must have a single data dependency
rms(x)	Root Mean Square of vector elements
runavg(x)	Running average of vector elements
stddev(x)	Standard deviation of vector elements
variance(x)	Variance of vector elements
random()	Random number between 0.0 and 1.0
srandom(x)	Give random seed

### Data Analysis: Basic Operation
cumprod(x)	Cumulative product of vector elements
cumsum(x)	Cumulative sum of vector elements
interpolate(f,x[,n])	Equidistant spline interpolation of real function vector f(x) using n equidistant datapoints; the latter can be omitted and defaults to a reasonable value
prod(x)	Product of vector elements
sum(x)	Sum of vector elements
xvalue(f,yval)	Returns the x-value which is associated with the y-value nearest to a specified y-value yval in a given vector f; therefore the vector f must have a single data dependency
yvalue(f,xval)	Returns the y-value of the given vector f which is located nearest to the x-value xval; therefore the vector f must have a single data dependency

### Data Analysis: Differentiation and Integration
ddx(expr,var)	Derives mathematical expression expr with respect to the variable var
diff(y,x[,n])	Differentiate vector y with respect to vector x n times. If n is omitted it defaults to n = 1
integrate(x,h)	Integrate vector x numerically assuming a constant step-size h

### Data Analysis: Signal Processing
dft(x)	Discrete Fourier Transform of vector x
fft(x)	Fast Fourier Transform of vector x
fftshift(x)	Shuffles the FFT values of vector x in order to move the frequency 0 to the center of the vector
Freq2Time(V,f)	Inverse Discrete Fourier Transform of function V(f) interpreting it physically
idft(x)	Inverse Discrete Fourier Transform of vector x
ifft(x)	Inverse Fast Fourier Transform of vector x
kbd(x[,n])	Kaiser-Bessel derived window
Time2Freq(v,t)	Discrete Fourier Transform of function v(t) interpreting it physically

## Electronics Functions
### Unit Conversion
dB(x)	dB value
dbm(x)	Convert voltage to power in dBm
dbm2w(x)	Convert power in dBm to power in Watts
w2dbm(x)	Convert power in Watts to power in dBm
vt(t)	Thermal voltage for a given temperature t in Kelvin

### Reflection Coefficients and VSWR
rtoswr(x)	Converts reflection coefficient to voltage standing wave ratio (VSWR)
rtoy(x[,zref])	Converts reflection coefficient to admittance; by default reference zref is 50 ohms
rtoz(x[,zref])	Converts reflection coefficient to impedance; by default reference zref is 50 ohms
ytor(x[,zref])	Converts admittance to reflection coefficient; by default reference zref is 50 ohms
ztor(x[,zref])	Converts impedance to reflection coefficient; by default reference zref is 50 ohms

### N-Port Matrix Conversions
stos(s,zref[,z0])	Converts S-parameter matrix to S-parameter matrix with different reference impedance(s)
stoy(s[,zref])	Converts S-parameter matrix to Y-parameter matrix
stoz(s[,zref])	Converts S-parameter matrix to Z-parameter matrix
twoport(m,from,to)	Converts a two-port matrix from one representation into another, possible values for from and to are 'Y', 'Z', 'H', 'G', 'A', 'S' and 'T'.
ytos(y[,z0])	Converts Y-parameter matrix to S-parameter matrix
ytoz(y)	Converts Y-parameter matrix to Z-parameter matrix
ztos(z[,z0])	Converts Z-parameter matrix to S-parameter matrix
ztoy(z)	Converts Z-parameter matrix to Y-parameter matrix

### Amplifiers
GaCircle(s,Ga[,arcs])	Circle(s) with constant available power gain Ga in the source plane
GpCircle(s,Gp[,arcs])	Circle(s) with constant operating power gain Gp in the load plane
Mu(s)	Mu stability factor of a two-port S-parameter matrix
Mu2(s)	Mu' stability factor of a two-port S-parameter matrix
NoiseCircle(Sopt, Fmin,Rn,F[,Arcs])	Generates circle(s) with constant Noise Figure(s) F. Arcs specifies the angles in degrees created by e.g. linspace(0,360,100). If Arcs is a number it specifies the number of equally spaced circle segments, if it is omitted this number defaults to a reasonable value
PlotVs(data,dep)	Returns a data item based upon vector or matrix vector data with dependency on a given vector dep, e.g. PlotVs(Gain,frequency/1e9)
Rollet(s)	Rollet stability factor of a two-port S-parameter matrix
StabCircleL(s[,arcs])	Stability circle in the load plane
StabCircleS(s[,arcs])	Stability circle in the source plane
StabFactor(s)	Stability factor of a two-port S-parameter matrix. Synonym for Rollet()
StabMeasure(s)	Stability measure B1 of a two-port S-parameter matrix

## Nomenclature
### Ranges
LO:HI	Range from LO to HI
:HI	Up to HI
LO:	From LO
:	No range limitations

### Matrices and Matrix Elements
M	The whole matrix M
M[2,3]	Element being in 2nd row and 3rd column of matrix M
M[:,3]	Vector consisting of 3rd column of matrix M

### Immediate
2.5	Real number
1.4+j5.1	Complex number
[1,3,5,7]	Vector
[11,12;21,22]	Matrix

### Number suffixes
E	exa, * 1e+18
P	peta, * 1e+15
T	tera, * 1e+12
G	giga, * 1e+9
M	mega, * 1e+6
k	kilo, * 1e+3
m	milli, * 1e-3
u	micro, * 1e-6
n	nano, * 1e-9
p	pico, * 1e-12
f	femto, * 1e-15
a	atto, * 1e-18

### Name of Values
S[1,1]	S-parameter value
nodename.V	DC voltage at node nodename
name.I	DC current through component name
nodename.v	AC voltage at node nodename
name.i	AC current through component name
nodename.vn	AC noise voltage at node nodename
name.in	AC noise current through component name
nodename.Vt	Transient voltage at node nodename
name.It	Transient current through component name

Note: All voltages and currents are peak values.
Note: Noise voltages are RMS values at 1 Hz bandwidth.
## Constants
i, j	Imaginary unit ("square root of -1")
pi	4*arctan(1) = 3.14159...
e	Euler = 2.71828...
kB	Boltzmann constant = 1.38065e-23 J/K
q	Elementary charge = 1.6021765e-19 C

back to the top